Proton Acceleration in Dielectric Structure: Simulation Tool
Semester thesis by
Max Kellermeier
maxk@student.ethz.ch
Andreas Adelmann
Rasmus Ischebeck
Eugenio Ferrari

---
Overview
Long Term Goal: Laser Driven Acceleration of Protons in a Dielectric Structure
- For highly relativistic particles
- For slow particles
Semester project:
- Development of a simplified simulation tool
  → limited by the choice of geometry
- Finding lower limit of β
- Parameter study
Chosen Geometry: Cylindric Waveguide with dielectric loading [1]
[1] E.A. Nanni et. al., Linear Electron Acceleration in THz Waveguides, Proceedings of IPAC2014, Dresden

---
Assumptions for the DLA
Three parameters:
- Inner radius a
- Outer radius b
- Dielectric permittivity
- Outer Material: Perfect conductor → no parallel electric field on surface
- Power losses in dielectric neglected → field not damped
- Infinitely extended structure → no boundary effects

---
Assumptions about field and beam interaction
- Acceleration with fundamental mode TM01
- Electromagnetic field continuous (not pulsed)
  → Timing of beam and laser neglected
- Single particle treatment → no space charge effects
- Energy gain small
  - Constant velocity during integration
  - Constant reference momentum in computing Twiss parameters

---
Field Distribution and Field Dispersion
Analytical solution for radial dep.: Bessel functions J0, Y0 [1]
Limit cases:
- no loading
- fully loaded
→ phase velocity above c for unloaded waveguide
→ low phase velocity in fully loaded waveguide
\omega = \dfrac{c}{ \sqrt{\epsilon_r}} \sqrt{k^2 + \gamma^2}
[1] W. Gai, C. Jing, Dielectric Loaded Accelerating Structures, in Periodic Structures, 2006

---
Varying DLA Parameters

---
Varying DLA Parameters

---
Varying DLA Parameters

---
Varying DLA Parameters
smaller inner radius / larger outer radius lowers phase velocity
→ trade of between particle loss and laser power loss

---
Simulation Tool
Live Demo