## Slide 1: Chip design for dummies
Roberto Dinapoli :: NUM/SLS Detector Group :: Paul Scherrer Institut
LTP Mini review Talk :: 11.12.2017

## Slide 2: Outline
Introduction:which electronics?
The ASIC
  building blocks
  design flow
  a simple exercise
  design for radiation tolerance
Chip design at PSI
  origins and present situation
  technologies
  some achievements
Conclusions

## Slide 3: Electronics: but which one ??
Discrete electronics

## Slide 4: Electronics: but which one ??
“Off the shelf” components

## Slide 5: Electronics: but which one ??
Programmable devices

## Slide 6: Electronics: but which one ??
Application Specific Integrated Circuit (ASIC)
Replica of the first point-contact transistor by Bardeen, Brattain and Shockley (Bell Labs,1947)
First planar transistor by the swiss Jean Hoerni (Fairchild,1959)
First integrated circuit developed by Jack Kilby (TI,1958)
IEEE spectrum 03.2017 : “Intel Now Packs 100 Million Transistors in Each Square Millimeter”

## Slide 7: Electronics: but which one ??
Application Specific Integrated Circuit (ASIC)
Standard cells/IP blocks
Full custom chip
  expensive
  time consuming/long turnaround times
  designers with specific skills needed
  tailored to the user’s needs:
    peculiar application
    analogue and digital on the same chip
    radiation tolerance
    very high transistor density

## Slide 8: The ASIC building blocks
P-type MOS-FET
N-type MOS-FET
Resistor
Capacitor
Wire
Inductor

## Slide 9: The transistor (super)basics
DIGITAL VIEW:
Microscopic switch
vg
v=0V
v=2V
Analog VIEW:
Controlled source/amplifier
vg
Id~vg
Id
Id =K* W/L * vg

## Slide 10: Chip design flow: schematic and simulation
Design specifications
Technology information
Transistor and device models
Computer simulations
(Spectre)
Block diagram analysis
(Mathematica,matlab)
output waveforms
Layout
Schematic view
Simulated circuit parameters:
Gain, noise, speed, variability,
sensitivity…

## Slide 11: Simple exercise: an inverter

## Slide 12: Simple exercise: an inverter

## Slide 16: Simple exercise: an inverter

## Slide 17: Simple exercise: an inverter

## Slide 18: Simple exercise: an inverter

## Slide 19: Simple exercise: an inverter

## Slide 20: Simple exercise: an inverter

## Slide 21: Simple exercise: an inverter

## Slide 22: Fabrication process flow, basic steps
Process steps required for patterning of silicon dioxide.

## Slide 23: Fabrication process flow, NMOS transistor
Process steps required for generating an NMOS transistor

## Slide 24: Fabrication process flow, NMOS transistor
Process steps required for generating an NMOS transistor

## Slide 25
P-type silicon
N-type silicon
Transistor implantation
P-type transistor
Transistor gate
(polysilicon)
Contact to
polysilicon
Contact to
implantation
Contact to
implantation
Contact to
well
W
L
Source
Drain
Source
Drain
Well
Well
Gate
Fabrication process flow, PMOS transistor

## Slide 26: Simple exercise: an inverter

## Slide 27: Simple exercise: an inverter

## Slide 28: Chip design flow: Design Rules Check (DRC)

## Slide 29: Chip design flow: Layout vs Schematic (LVS)
?
=
Netlist Layout
Netlist Schematic
Comparison
Correct!
LVS

## Slide 30: Chip design flow: Layout vs Schematic (LVS)
?
=
Netlist Layout
Netlist Schematic
Comparison
Correct!
LVS
Netlist with parasitics
LVS + PEX
(paras.extr.)

## Slide 31: The ASIC building blocks
Metal
connections
Very old technology: AMS 0.8μm BICMOS

## Slide 32: The challenge of LHC inner trackers
Challenges:
High performance
High radiation tolerance
Low power consumption
High density …
Components “off the shelf”
Radiation hard technologies
Design for radiation tolerance

## Slide 33
Thin Oxide-NMOS Transistors in enclosed geometry
Design implications !
W/L limitation
Transistor modeling
Density
Libraries
Verification routines
Thin Oxide (<6nm) improves radiation tolerance
Enclosed geometry transistors and guard-rings prevent from radiation induced leakage
N+
D
S
L
W
L
W
What made LHC inner trackers possible (and affordable): Design for Radiation Tolerance

## Slide 34: Chip design flow: “final” steps
Full chip layout assembly
Wafer dicing
Chip global checks
Chip packaging/post-processing
Tape out
Wafer post processing
FOUNDRY
(UMC)
13.5 mm
15.8 mm
ALICE1LHCb
WAFER

## Slide 35
PART II: Chip design at PSI

## Slide 36: Origin of chip design at PSI
PSI46
DRS 2
PILATUS II
CMS
ITS
Spinoff company: Dectris LTD
Sept. 2006
SLS
LHC
MEG
MYTHEN II

## Slide 37
CMS
MEG
SLS Detectors
Others
Department: NUM
Lab:Particle Physics Group:Electronics
Chip Design
Core Team
X.Shi (Sw.FEL)
B.Meier (NUM)
R.Dinapoli (NUM)
A.Mozzanica (Sw.FEL)
D.Mezza (NUM/SYN)
Chip design at PSI: Organization
Most of our design work concerns:
Design of radiation tolerant front end chips for strip and hybrid pixel detectors both for HEP and for photon science

## Slide 38: Chip Design Core Team: Tasks
CAD support
Students training
Interface with EP/MOSIS
DESIGN
Chip Design
Core Team
(CDCT)
Technical advice
Technology setup
Building blocks
Full chip
Conferences and publications
Patent filing – Spin offs

## Slide 39: EIGER
EIGER: next generation single photon counting detector for X-Ray applications
2 cm
Technological process | UMC 0.25 µm, full rad tol design
Analog Parameters | 30 ns peaking time, ~150 ns ret. Zero 130e- rms ENC
Chip size | 19.3 x 20.1 mm2 , 28M transistor
Pixel size | 75 x 75 µm2
Pixel array | 256 x 256 = 65536
Count rate | 3.4 x 109 x-rays/mm2/s (1-2 Mcounts/pixel/s)
Counter | 12 bits, configurable,double buffered
Frame rate | Up to 23 kHz (in 4 bit mode)

## Slide 40: EIGER X-ray absorption image
No stitching, no trimming, with background correction
2cm
4cm
8cm
(High Frame Rate Demo)

## Slide 41
  MODULE
  500 k pixel
  38 X 77 mm2
  8 GB memory
Towads bigger systems
9M EIGER DETECTOR
Area: 23x23cm2
Number of pixels: 9 million
Frame rate: up to 23 kHz
Developed for SLS cSAXS beamline
Total (raw) data rate: 900Gb/s
Notes: Cu tube, 25kV, 80mA, pinhole, 1.5m distance

## Slide 43: An Eiger self portrait (Ptychography)
Diffraction pattern
from one ½ of a module
Object:
Eiger readout chip
The object is raster scanned
by an out of focus beam
Diffraction patterns at
overlapping positions on the
object are recorded
The information in the overlap
is used to recover the dp phase
Both the attenuation and phase
shift in the object can be
reconstructed
Phase image
OSA
Object
FZP
Coherent X-rays
80 um

## Slide 44
Open access link: http://rdcu.be/p7bi

## Slide 45: MÖNCH
Currently 1x1 cm2 prototype available
  400x400=160 kpixel
Fast frame rate (> kHz)
  currently 3 kHz
  by design 6 kHz
  Ca. 20 TB/day
Dead-time free operation possible
M. Ramilli, et al. (2017) J. Instr. 12, C01071.http://dx.doi.org/10.1088/1748-0221/12/01/C01071
Micropixel with enhanced pOsition rEsolution usiNg CHarge integration
Small pixels 25 x 25 μm2
  Bump bonding works!
Low noise
  320 eV energy resolution FWHM
Large dynamic range
  Up to now statically selectable
  Will have adaptive gain
Pilatus 172 μm
Eiger 75 μm
x5.3
Mönch 25 μm
x47

## Slide 46: Charge sharing – Spatial resolution
High resolution digital image
Low resolution analog image
Charge sharing
Division of charge between pixels is strongly position dependent
Can improve the spatial resolution
  Pitch ≈ charge sharing distance
    320 µm thick Si, 120V ≈ 20 µm
    Depends on the drift time:
      Applied bias voltage
      Absorption depth
        Sensor thickness
        X-ray energy
  High SNR
    Low noise
  Isolated photons
    Fast frame rate
    Low flux
“Single shot x-ray phase contrast imaging using a direct conversion microstrip detector with single photon sensitivity” Kagias, M., Cartier, S., Wang, Z., Bergamaschi, A., Dinapoli, R., Mozzanica, A., Schmitt, B. & Stampanoni, M. (2016). Appl. Phys. Lett. 108, 234102.

## Slide 47: High resolution imaging
25 µm pixels
Interpolated
SOLEIL, Nanoscopium
11 keV
Siemens star
2 µm bins
Synchrotron
W-tube
55kV
EIGER HDI
5 µm bins
X-ray tube
SLS, PHOENIX
2 keV
61µm pitch metal grid
1 µm bins
Low energy
100µm

## Slide 48: Conclusions
Despite the complexity, an ASIC can be the only viable solution for specific requirements
PSI chip design group based on “matrix architecture”, successful model
Several chips already developed for different applications, some spinned-off
Many developments going on for LHC, M3E, synchrotron and most of all for free-electron laser applications

## Slide 49
THANKS!

## Slide 50: Chip design at PSI: particle detection systems
Particle physics
CMS
MEG
Pixel chip for the inner tracker (PSI46)
New version for LHC luminosity upgrade
Domino sampling chips (DRS4)
New version for MEEE (DRS5)
X-ray detection
(SLS Detectors)
Synchrotrons
XFELs
Pilatus (SPC)
Eiger (SPC)
Mönch (INT)
Mythen (SPC)
Gotthard (INT)
AGIPD (INT)
Mönch (INT)
Pixels (2D)
Strips (1D)
Gotthard (INT)
Jungfrau (INT)
SPC= single photon counting INT=charge integration
HiZ – Neutron – Low energy X-ray –Electron – Space – detectors
Small pitch bump-bonding
Research

## Slide 51: The basic principle of hybrid pixel detectors
A silicon detector
bump-bonded with a readout chip
Detector substrate
Electronics substrate
p implant
p implant
Electronics
Electronics
n-diffusion
Contact metal pads
Bump-bond
Pb-Sn Bump Bond
Bump bond metal pad

## Slide 52: The basic principle of hybrid pixel detectors
Amplifier
Shaper
Incoming particle
Induced
Current
Discriminator
Logic
Amplifier
CDS
Incoming particle
Induced
Current
Buffer
Events counting
Analog readout

## Slide 53: Requirements for an ideal detector
  Single photon resolution
  No spatial distortion and uniform response
  Large dynamic range
  Large area
EIGER
  Small pixel size
  Small dead area
  Fast Frame Rate
  Simultaneous exposure and readout
  Negligible dead time
  High count rate of incoming photons
PILATUS
+

## Slide 54: An Eiger self portrait (Ptychography)
Diffraction pattern
from one ½ of a module
Object:
Eiger readout chip
The object is raster scanned
by an out of focus beam
Diffraction patterns at
overlapping positions on the
object are recorded
The information in the overlap
is used to recover the dp phase
Both the attenuation and phase
shift in the object can be
reconstructed
Phase image
OSA
Object
FZP
Coherent X-rays
80 um

## Slide 55: Large area, high resolution Ptychography
5 um
0.5 x 0.5 mm2
Zoom in on a pixel
~50 nm resolution

## Slide 56: Large area, high resolution Ptychography
5 um
Zoom in on a pixel
0.5 x 0.5 mm2
~50 nm resolution
Notes: Green- implant
Red- poly silicon
Blue- metal