## Slide 1: Laser heater at SwissFEL
S. Bettoni
A.Dax, M.Huppert, C. Vicario

## Slide 2: Outlook
Laser heater characterization and calibration:
  Longitudinal and transverse overlap laser- e- beam
  Induced energy spread
  Heating of the bunch: shaping and uniformity along the bunch (at the injector)
Microbunching at the injector:
  Structures along the pulse for several compression factors
  Effect of the laser heater
Impact of the laser heater at the end of the machine (feed-backs closed):
  Heating along the bunch (at the injector)
  FEL intensity as a function of the LH intensity
  Some considerations about the measurements setup
Bunch generated using the stretched Alcor:
  Scan of the pulse length vs charge
  Structures along the pulse for several compression factors
  Effect of the microbunching on the monitors in the compression feed-backs
KAs beams
  Slice energy spread as a function of the compression factor and slice energy spread at the injector
  Microbunching
Impact of the laser heater at the end of the machine(feed-backs open):
  Heating along the bunch (at SARCL)
  FEL intensity as a function of the LH intensity
Conclusions
Jaguar
Stretched Alcor (Gaussian)

## Slide 3: Outlook
Laser heater characterization and calibration:
  Longitudinal and transverse overlap laser- e- beam
  Induced energy spread
  Heating of the bunch: shaping and uniformity along the bunch (at the injector)
Microbunching at the injector:
  Structures along the pulse for several compression factors
  Effect of the laser heater
Impact of the laser heater at the end of the machine (feed-backs closed):
  Heating along the bunch (at the injector)
  FEL intensity as a function of the LH intensity
  Some considerations about the measurements setup
Bunch generated using the stretched Alcor:
  Scan of the pulse length vs charge
  Structures along the pulse for several compression factors
  Effect of the microbunching on the monitors in the compression feed-backs
KAs beams
  Slice energy spread as a function of the compression factor and slice energy spread at the injector
  Microbunching
Impact of the laser heater at the end of the machine(feed-backs open):
  Heating along the bunch (at SARCL)
  FEL intensity as a function of the LH intensity
Conclusions
Jaguar
Stretched Alcor (Gaussian)

## Slide 4: Transverse laser vs e- alignment
Enabled the feed-back for e- and laser (?)
Both beams observed on the Chromox screen
Only e-
Only laser
DSCR220
DSCR250
 | DSCR220 | DSCR250
X | 38% | 20%
Y | 45% | 18%
Beam sizes difference (photons vs e-):

## Slide 5: K optimization
Scan of the K of the undulator looking at the induced energy spread
Scan performed using the Alcor laser to heat the beam
sinc(K) expected

## Slide 6: Beam heating
FERMI
LCLS
SwissFEL
Core beam
Projected beam
SWISSFEL
LH laser: Jaguar
Injector laser: Alcor
Baseline energy reader

## Slide 7: Slice energy spread at the injector
Increasing laser energy
Granularity of the induced energy spread: step size<0.5 keV
DE ~ 6.4 keV for PLaser = 0 uJ

## Slide 8: Beam heating along the bunch
SwissFEL
It seems that we have already a good “heating shape”
Another day tried with other 2 beam sizes, and the best heating with the first one
Check if the laser and the e- beam spot size are at the correct values (transverse)

## Slide 9: LH AND injector laser: analysis
To determine the heating along the bunch:
  I cut in y
  I compute the profile in x at each selected y
  I determine sigma_x (proportional to energy spread via dispersion)
N slices = 100

## Slide 10: Heating along the bunch (LH-Jaguar)
More precise analysis:
  I cut in y
  I compute the profile in x at each selected y
  I plot the sigma_x (proportional to energy spread via dispersion)
LH off
LH on
LH laser: Jaguar
Injector laser: Alcor

## Slide 11: Heating along the bunch (LH-Alcor)
I cut in y
I compute the profile in x at each selected y
I do Gauss fit
LH off
LH on
Uniform heating along the bunch
LH laser: Alcor
Injector laser: Alcor

## Slide 12: Outlook
Laser heater characterization and calibration:
  Longitudinal and transverse overlap laser- e- beam
  Induced energy spread
  Heating of the bunch: shaping and uniformity along the bunch (at the injector)
Microbunching at the injector:
  Structures along the pulse for several compression factors
  Effect of the laser heater
Impact of the laser heater at the end of the machine (feed-backs closed):
  Heating along the bunch (at the injector)
  FEL intensity as a function of the LH intensity
  Some considerations about the measurements setup
Bunch generated using the stretched Alcor:
  Scan of the pulse length vs charge
  Structures along the pulse for several compression factors
  Effect of the microbunching on the monitors in the compression feed-backs
KAs beams
  Slice energy spread as a function of the compression factor and slice energy spread at the injector
  Microbunching
Impact of the laser heater at the end of the machine(feed-backs open):
  Heating along the bunch (at SARCL)
  FEL intensity as a function of the LH intensity
Conclusions
Jaguar
Stretched Alcor (Gaussian)

## Slide 13: Structures vs compression
Change the compression factor at BC1 and I measure at the injector spectrometer
I change the compression factor (fixed R56), so I modify the equivalent time step on the spectro screen
 same “read” frequency  the f of the structure scales exactly with the compression factor

## Slide 14: Longitudinal phase space injector
Peak current ~160 A from 14 A: CF = 11.5
Q = 200 pC, E = 300 MeV
S10BD01-MQUA010: 14.428 A
We observe some structures with the Jaguar, but only in energy, not in time

## Slide 15: Energy vs time correspondence
A way to retrieve the time (and frequency) information
2.5 ps (p2p) corresponds to 240 pixel at the TDC screen
The bunch length does not change between the TDC screen and the spectrometer screen
At the spectrometer screen 2000 pixels correspond to 2.5 ps
The structures are tilted to be perpendicular to the x (energy) axis
One pixel corresponds to 1.25 fs at the spectrometer screen
I use this info to compute the frequency of the modulation
7.4% amplitude modulation

## Slide 16: Comparison to model
I normalize the profile to have integral 200 pC
I remove the smoothed profile
I compute the equivalent current modulation and fft
I select the window of integration
I multiply the wavelength by the compression factor at BC1 to compute that at the cathode
ANALYSIS
Cs2Te has a response time ~1 ps (1 THz-300 um), so all the components with periodicity<300 um are expected to be damped more than with copper
With Cu different dynamics expected (response time ~few hundreds fs): more structures at wavelength<300 um expected
MEASURMENTS RESULTS
SIMULATIONS
Assumed compression factor = 10

## Slide 17: LH off vs LH on
The laser heater efficiently damps the modulations (we do not know the distribution of the noise on the initial distribution)
Comment about the resolution: 1.25 fs  0.37 um. If I want 5 points to define the modulation  1.85 um visible  18.5 um at the cathode
MEASURMENTS RESULTS
SIMULATIONS
Assumed compression factor = 10

## Slide 18: Time plane
It seems to be “only” some noise in time

## Slide 19: Laser heater impact: more in detail
Zoom (change of the ROI) on the bunch at the injector spectrometer
Scan of the LH laser energy for different filters (large step size) and changing the wave plate (fine tuning)
LH off
LH on

## Slide 20: Modulations vs LH intensity-energy plane
ND = 0
ND = 2
ND = 4
ND = 0.5

## Slide 21: Modulations vs LH intensity-energy plane
Filter ND = 0.5
Filter ND = 0
Filter ND = 2
Filter ND = 4
Dependency on the intensity of the laser heater
Overlap among the different cases
Filter ND = 0.5

## Slide 22: Modulations vs LH intensity-time plane
Some noise observed: not related to the LH on or off
Filter ND = 0
Filter ND = 4
Filter ND = 4

## Slide 23: Outlook
Laser heater characterization and calibration:
  Longitudinal and transverse overlap laser- e- beam
  Induced energy spread
  Heating of the bunch: shaping and uniformity along the bunch (at the injector)
Microbunching at the injector:
  Structures along the pulse for several compression factors
  Effect of the laser heater
Impact of the laser heater at the end of the machine (feed-backs closed):
  Heating along the bunch (at the injector)
  FEL intensity as a function of the LH intensity
  Some considerations about the measurements setup
Bunch generated using the stretched Alcor:
  Scan of the pulse length vs charge
  Structures along the pulse for several compression factors
  Effect of the microbunching on the monitors in the compression feed-backs
KAs beams
  Slice energy spread as a function of the compression factor and slice energy spread at the injector
  Microbunching
Impact of the laser heater at the end of the machine(feed-backs open):
  Heating along the bunch (at SARCL)
  FEL intensity as a function of the LH intensity
Conclusions
Jaguar
Stretched Alcor (Gaussian)

## Slide 24: LH and lasing
In both cases not positive effect of the LH on the lasing
May
July

## Slide 25: Heating at the end of the machine
Measurement of the slice energy spread at SARCL02:
  Scan over the energy of the LH laser intensity
  Scan over the filters
Index increasing
3 kA beam

## Slide 26: Heating-end of the machine-E plane
Filter ND = 0.5
Filter ND = 1

## Slide 27: Heating-end of the machine-t plane
Filter ND = 1
Filter ND = 1
Filter ND = 0.3

## Slide 28: Heating along the bunch-end of the machine
I cut in y (time) direction
I compute the profile in x (energy) at each selected y
I compute a Gaussian fit
I plot the sigma of the fit
I artificially shifted the plots
Kind of uniform heating along the bunch length
Increase of the energy spread at the head of the bunch increasing the laser intensity

## Slide 29: Large intensity of the LH laser
Index = 1
Index = 26
Observed a kind of explosion of the beam at the head increasing the intensity of the laser heater

## Slide 30: Bunch length change during the scans
The LH damps the structures along the bunch
The reading of the compression monitor is reduced (not readable from Archiver-to be checked)
The compression feed-back (only BC1 in May and both in July) compress more the bunch
We move away from the optimum point for lasing (tapering, CSR kick, wakefield, …)

## Slide 31: Outlook
Laser heater characterization and calibration:
  Longitudinal and transverse overlap laser- e- beam
  Induced energy spread
  Heating of the bunch: shaping and uniformity along the bunch (at the injector)
Microbunching at the injector:
  Structures along the pulse for several compression factors
  Effect of the laser heater
Impact of the laser heater at the end of the machine (feed-backs closed):
  Heating along the bunch (at the injector)
  FEL intensity as a function of the LH intensity
  Some considerations about the measurements setup
Bunch generated using the stretched Alcor:
  Scan of the pulse length vs charge
  Structures along the pulse for several compression factors
  Effect of the microbunching on the monitors in the compression feed-backs
KAs beams
  Slice energy spread as a function of the compression factor and slice energy spread at the injector
  Microbunching
Impact of the laser heater at the end of the machine(feed-backs open):
  Heating along the bunch (at SARCL)
  FEL intensity as a function of the LH intensity
Conclusions
Jaguar
Stretched Alcor (Gaussian)

## Slide 32: Bunch and laser at BC1 (uncompressed)
Q = 200 pC, BC1 straight, 90 degs in SINSB03/04, no SINXB, E = 300 MeV
Similar length as the cross-co measurement (different with Jaguar)

## Slide 33: Pulse length for several charges
Q (pC) | Sigma_t (ps)
200 | 3.34
100 | 2.91
50 | 2.61
Cross co | 3.23
Q = 100 pC
Q = 50 pC

## Slide 34: Some halo?
Observed some halo or screen effect?
Uncompressed bunches, BC1 straight, beam on crest
Q = 100 pC
Q = 50 pC
Q = 200 pC

## Slide 35: Several bunch lengths, profiles
Sigma_t = 170 fs
Sigma_t = 250 fs
Sigma_t = 620 fs
Sigma_t = 1.37 ps
I scan the compression factor and I measure the longitudinal current profile

## Slide 36: LH off/LH on
I do the fft of the longitudinal profile removed the smoothed part
Less pronounced the structures compared to the Jaguar laser at similar compression factor
LH off
LH on

## Slide 37: Outlook
Laser heater characterization and calibration:
  Longitudinal and transverse overlap laser- e- beam
  Induced energy spread
  Heating of the bunch: shaping and uniformity along the bunch (at the injector)
Microbunching at the injector:
  Structures along the pulse for several compression factors
  Effect of the laser heater
Impact of the laser heater at the end of the machine (feed-backs closed):
  Heating along the bunch (at the injector)
  FEL intensity as a function of the LH intensity
  Some considerations about the measurements setup
Bunch generated using the stretched Alcor:
  Scan of the pulse length vs charge
  Structures along the pulse for several compression factors
KAs beams
  Effect of the microbunching on the monitors in the compression feed-backs
  Heating along the bunch
  Slice energy spread as a function of the current
Impact of the laser heater at the end of the machine(feed-backs open):
  Heating along the bunch (at SARCL)
  FEL intensity as a function of the LH intensity
Conclusions
Jaguar
Stretched Alcor (Gaussian)

## Slide 38: Beam in SARCL02
E
t
Elegant simulations

## Slide 39: Compression monitors: BC1
For sigma_t = 0.17 ps and 1.37 ps I scan the compression monitor reading in BC1 vs the laser heater energy:7981 and 7982
No appreciable effect

## Slide 40: Compression monitors: BC2
Set-up the 3 kA beam and scan of the energy of the laser LH intensity
Sensitive at BC2
Filter automatically inserted during the scan

## Slide 41: kAs beam
I change the compression factor (nominal peak current and more) to try to enhance the microbunching structures
I = 3.2 kA, FWHM ~92 fs
I = 5.5 kA, FWHM ~33 fs
Not appreciable enhancement observed

## Slide 42: Heating along the bunch-SARCL02
Verify that we are still heating uniformly the beam along its length
Point 1: minimum LH intensity
Point 23: high LH intensity
Point 12: intermediate
I do not do the fit if the intensity is below a threshold

## Slide 43: Outlook
Laser heater characterization and calibration:
  Longitudinal and transverse overlap laser- e- beam
  Induced energy spread
  Heating of the bunch: shaping and uniformity along the bunch (at the injector)
Microbunching at the injector:
  Structures along the pulse for several compression factors
  Effect of the laser heater
Impact of the laser heater at the end of the machine (feed-backs closed):
  Heating along the bunch (at the injector)
  FEL intensity as a function of the LH intensity
  Some considerations about the measurements setup
Bunch generated using the stretched Alcor:
  Scan of the pulse length vs charge
  Structures along the pulse for several compression factors
  Effect of the microbunching on the monitors in the compression feed-backs
KAs beams
  Slice energy spread as a function of the compression factor and slice energy spread at the injector
  Microbunching
Impact of the laser heater at the end of the machine(feed-backs open):
  Heating along the bunch (at SARCL)
  FEL intensity as a function of the LH intensity
Conclusions
Jaguar
Stretched Alcor (Gaussian)

## Slide 44: Compression settings-SARCL02
Feed-back = 2000
Feed-back = 2550
Feed-back = 3500
Feed-back = 1519 (lasing)

## Slide 45: Slice energy spread
For the different compression factors measured the slice energy spread at SARCL02
Resolution limit ~ 1 MeV
Assumed dispersion = 0.1 m (corrected from previous slide plots)
New optics with D = 0.4 m to improve the resolution

## Slide 46: FEL scans-lasing beam
I measure the FEL intensity (fast signal) as a function of the laser intensity of the LH
Scan repeated for several filters
I ~ 1 kA

## Slide 47: FEL scans at feed-back 3500
I measure the FEL intensity (fast signal) as a function of the laser intensity of the LH
Scan repeated for several filters

## Slide 48: Conclusions
  Microbunching instability seems to be smaller than expected assuming instantaneous photoemission:
    Spectral analysis shows qualitative agreement with the model response of the machine
    Analysis at SARCL02 did not show evidence of structures neither in energy nor in time (resolution limited?)
    Some structures visible using SRM and they are damped using the LH
  Laser heater commissioning:
    Setup completed:
      Longitudinal and transverse alignments done
      Induced energy spread as a function of the laser energy measured
    The system produces uniform heating along the bunch : measurements at injector spectrometer and at SARCL02
    The system is powerful enough to dump the energy structures (step size also good-less than 0.5 keV)
    Repeated the measurements using the stretched Alcor instead of the Jaguar: similar conclusions, but for Jaguar less pronounced structures (to be checked again for confirmation)
  Effect of the laser heater on the microbunching instability:
    FEL intensity is not increased by the laser heater: scans repeated for several peak currents and lasers
  More measurements:
    More “straight forward” measurements:
      Measurements at SARCL02 using new optics x4 dispersion to improve the resolution, useful also for compression scans
    More demanding but “answering” measurements:
      Spectral content and FEL scan using a copper cathode
Microbunching instability is less detrimental than expected from simulations, where 0 response time cathode were assumed

## Slide 49: Conclusions
  Microbunching instability seems to be smaller than expected assuming instantaneous photoemission :
    Spectral analysis shows qualitative agreement with the model response of the machine
    Analysis at SARCL02 did not show evidence of structures neither in energy nor in time (resolution limited?)
    Some structures visible using SRM and they are damped using the LH
  Laser heater commissioning:
    Setup completed:
      Longitudinal and transverse alignments done
      Induced energy spread as a function of the laser energy measured
    The system produces uniform heating along the bunch : measurements at injector spectrometer and at SARCL02
    The system is powerful enough to dump the energy structures (step size also good-less than 0.5 keV)
    Repeated the measurements using the stretched Alcor instead of the Jaguar: similar conclusions, but for Jaguar less pronounced structures (to be checked again for confirmation)
  Effect of the laser heater on the microbunching instability:
    FEL intensity is not increased by the laser heater: scans repeated for several peak currents and lasers
  More measurements:
    More “straight forward” measurements:
      Measurements at SARCL02 using new optics x4 dispersion to improve the resolution, useful also for compression scans
    More demanding but “answering” measurements:
      Spectral content and FEL scan using a copper cathode
Microbunching instability is less detrimental than expected from simulations, where 0 response time cathode were assumed

## Slide 51: Measurements at SITF (with stacking)
Comparison Cu vs Cs2Te for different compression factors with the stacking
Cs2Te
Cu
SIMULATIONS
MEASUREMENTS
MEASUREMENTS
16 stacks
8 stacks

## Slide 52: Answers possible with Cu cathode
Best scenario: Cs2Te damps the microbuching in the range of frequency of high gain
Worst scenario: Cs2Te increases the slice energy spread
Instability is damped (at the e- emission), and we do not need LH to heat it
We have already high energy spread from the beginning
EXAMPLE PLOT
More intense microbunching instability at lambda~50 um or smaller wavelengths
Positive effect of the LH on FEL or not?

## Slide 53: LH more or less intense
Less laser intensity
More laser intensity

## Slide 54: “Equivalent” current profile
About 10 A over 135: 7.4%

## Slide 55: Some comments about Alcor
Uncompressed bunch very well optimized (optimizer by Martin)
If the optimization has to be done looking at the compressed bunch some modifications to the code are necessary (stabilization of the bunch)
Energy
Time
t
In this condition along the machine longitudinal phase space strongly deformed, like observed at SITF (LSC+compression). Possible to see the energy structures generated by the stacking.
LH off
LH on
Wavelength of the modulations:
  16 stacks  187.5 um
  8 stacks  375 um
  32 stacks  93.8 um
Energy

## Slide 56: Comparison Alcor vs Jaguar
Alcor
Jaguar
Energy spread to be multiplied by 9 (assumed dispersion = 0.9 m but it is 0.1 m)

## Slide 57: Compression settings-SARCL01
I check if the bunch length/peak current are correct at SARCL01
SARCL02
SARCL01
Feed-back at 3500
Feed-back at 2550

## Slide 58: Stacking wavelengths
Number of stacked pulses | Wavelength (um)
128 | 23.4
64 | 46.9
32 | 93.8
16 | 187.5
8 | 375.0

## Slide 59: Pulse profile and response time

## Slide 60: Slice energy spread vs peak current (July)
I change the compression factor and I measure the slice energy spread along the bunch

## Slide 61: Slice energy spread @ injector
From the compression factor I compute the expected slice energy spread at the injector
Blue: 3.9 ± 0.4 keV
Red: 4.20 ±0.07 keV
I average over ±5 slices around the central slice
I remove the contribution of the intercept

## Slide 62: Bunch compression (Jaguar)
Semi-analytical approach implemented in the machine (Dohlus et al., PRST-AB):
  Set-up of the desired compression factor
  Tuning of the 2nd order demonstrated
Target peak current (A)
Measured peak current (A)

## Slide 63: Estimation of the DE_0
I fit the induced energy spread as a function of the laser energy, and I compute the expected energy spread
The result indicates ~6 keV

## Slide 64: Beam heating optimized (May)
LH on
LH off
TDC on
TDC off
E
t
E
t
E
y
E
y

## Slide 65: Multi-stage bunch compression
Computation of the RF settings to compress the beam and shape the current profile known the current profile beam correlations (d*) and the machine energy profile (E*)
RF settings (unknowns)
Machine-beam parameters
Method which allows shaping the current profile:
  Knob 1: controls the compression factor
  Knob 2: controls the location of the peak current along the bunch
  Knob 3: controls the concavity

## Slide 66: Compression factor control
  Computed the RF settings given the machine and beam settings to have a given compression factor
  Discrepancy < 4% at compression factor of 12 (slightly better than the nominal 10) between set and obtained compression factor (if phases in the injector are properly set: error <0.1 deg)
  Energy at the compressors and downstream kept constant
  Quadrupoles scaled between SINSB04 and BC1 scaled: optics invariant
  Quadrupoles scaled between BC2 and S10CB08 (energy feed-back): optics invariant
Possible scans during the FEL optimization (starting setup)
Energy
Time

## Slide 67: Second order current control
Energy
Time
knob20
Knob20+D
Knob20-D

## Slide 68: Modulations vs LH intensity-time plane
Zoom
Filter ND = 0
Filter ND = 4
Same height and spread of the “modulations”: noise or not enough resolution

## Slide 69: LH on and off-heating
Lasers:
  Photoinjector: Alcor
  Laser heater: Jaguar
  index_y_start = 700; index_y_end = 1000; index_y_step = 25;
700
800
900
Pixel
Reconstructed the intensity variation of the Jaguar profile