## Slide 1: CBETA Beam optics based on Field Maps of the FFA-magnets*
* Work supported by the Department of Energy
N. Tsoupas, F. Méot, D. Trbojevic

## Slide 2: Outline
What is the CBETA accelerator
  Report on simple but very important ideas we introduced in the design of the CBETA accelerator
Description of the FFA cell
The field maps of the CBETA cell
Beam optics: (François Méot)
  Using the field maps of the CBETA cell
  Using the superposition of the field maps of the individual magnets of the CBETA cell

## Slide 3: The CBETA project is under commissioning at Cornell University It may serve as a prototype for the eRHIC project
Injection: 6 MeV e- 100 mA rep-rate 325 MHz
1.3 GHz 16 MV/m Emax~80 MeV
Beam dump
Splitter
Merger
Two remarkable concepts:
Energy Recovery Linac (ERL)
Fixed Field Alternating Gradient (FFAG)
Pass # | Energy
1 | 42
2 | 78
3 | 114
4 | 150
5 | 114
6 | 78
7 | 42
8 | 6
At any given time there is an equal number of accelerating
and decelerating bunces inside the ERL.
The Power of the Linac is minimal

## Slide 4: The concept of the CBETA FFAG cell
41 mm
Focusing
Quad
DeFocusing
Quad
Trajectories of e-bunches with different energy in a cell
A large energy range (42 MeV to 150 MeV) is confined in a small transverse distance of 41 mm
The De-Focusing Quad of the ARC is a Combined Function magnet Dipole+Quad
Each arc-cell bends the beam by 5o

## Slide 5: Number of the FFAG cells in the FFAG section of CBETA

## Slide 6
Placement of four FFAG cells on a girder
OPERA design of 3 cells
with Correctors
Single Halbach Magnet
with Corrector

## Slide 7: Some Concepts used in the CBETA accelerator
Energy Recovery Linac (ERL)
Fixed Field Alternating Gradient FFAG
Halbach type Permanent Magnets (PM)
Correctors around the PM
Wedges of variable R (S. Brooks)
Correction of Harmonics using
wires with high permeability ()

## Slide 8: Some advantage of using PM for the FFA
NO Cross talk between magnets (~1.0)
PM are Small size magnets
Strong fields with NO power supplies
Accepts correctors
Low cost vs. electromagnets.
Strong fields with NO power supplies

## Slide 9
Isometric view of Magnetized Wedges
Cross section of Magnetized Wedges of NdFeB or SmCo

Direction of the easy axis =(n+1) +/2
Dipole n=1
Quad n=2
Sext n=3

The Halbach Quadrupole
9/11

## Slide 11: Thank you for your attention

## Slide 14: Thank you for your attention

## Slide 15: Conclusions Halbach vs electromagnet
The Halbach magnet occupies smaller volume and can generates higher field in the same aperture.
It costs much less then the electromagnet.
It can be temperature controlled by water cooling.
It is subject to radiation damage.
  This is not a serious problem in the environment of 150 MeV electrons.
  The magnet will also be shielded for radiation damage.

## Slide 16: Thank you for your attention

## Slide 17: Introduction
Studies are under way at BNL for the design of an 18 GeV electron accelerator for the proposed eRHIC project.
eRHIC Detector
PHENIX
AGS
eRHIC
electron
ion
ion
Blue+Yellow=RHIC
Blue+Yellow+Red=eRHIC
Relativistic Heavy Ion Collider (RHIC)
250 MeV polarized protons
100 MeV/u Au-ions or other ions
5 to 18 GeV electrons

## Slide 18: Large fields in small volume magnet
Gap=3 cm W=30 cm H=18 cm Bmax~ 1 Tesla
Needs Power Supply and water for cooling
ri
rout

## Slide 19: Experimental proof of the field superposition for SmCo material
19/17
CAARI2016
The superposition is isotropic

## Slide 20: Large fields in small volume magnet
Gap=3 cm W=30 cm H=18 cm Bmax~ 1 Tesla
Needs Power Supply and water for cooling
ri
rout

## Slide 24: The CBETA project is under commissioning at Cornell University It may serve as a prototype for the eRHIC project
Injection: 6 MeV e- 100 mA rep-rate 325 MHz
1.3 GHz 16 MV/m Emax~80 MeV
Beam dump
Splitter
Merger
Two remarkable concepts:
Energy Recovery Linac (ERL)
Fixed Field Alternating Gradient (FFAG)
Pass # | Energy
1 | 42
2 | 78
3 | 114
4 | 150
5 | 114
6 | 78
7 | 42
8 | 6

## Slide 25: The CBETA project is a prototype for the eRHIC project
Injection: 6 MeV e- 100 mA rep-rate 325 MHz
1.3 GHz 16 MV/m ~80 MeV
Beam dump
Splitter
Merger
Two concepts: Energy Recovery Linac (ERL)
Fixed Field Alternating Gradient (FFAG)
Pass # | Energy
1 | 42
2 | 78
3 | 114
4 | 150
5 | 114
6 | 78
7 | 42
8 | 6
At any given time there is an equal number of accelerating
and decelerating bunces inside the ERL.
The Power of the ERL is minimal