## Slide 1: 2D Beam Profile Reconstruction in the ACHIP Chamber at SwissFEL Using Wire Scanners
Adrian Kirchner :: visiting student from FAU Erlangen :: Paul Scherrer Institute
SwissFEL Progress Meeting, 3.09.2019

## Slide 2: Current Status of ACHIP Chamber
Installed in-vacuum permanent magnet quadrupoles for achieving sub-micrometer beams
Content of this presentation: data analysis of beam size measurements

## Slide 3: Why Measure with Wire Scanners?
YAG-Screen resolution limit ≈ 10 μm [DOI: 10.1103/PhysRevSTAB.18.082802]
Planned experiments in ACHIP Chamber need sub-μm beams
Wire scanners are better choice for small beams, proven to work for beams with σ ≈ 0.46 μm [DOI: 10.1038/s42005-018-0048-x]
Electrons enter here
Opening of Structure: ~1 μm

## Slide 4: Multi-Dimensional Wire Scanners
Produced by LMN, thanks to Dr. Vitaliy Guzenko!
Mounted on hexapod
Allows measurement of arbitrary projection -> Reconstruct 2D profile

## Slide 5: Evaluating the Data: Fit Model
Convolution
Assumption: Intensity can be described by Gaussian distribution (2D and tilt)
Wire scan = Line integral of the beam intensity along the wire (Radon transform)
Convolution with wire profile
Radon Transform
2D Gaussian Profile (x_0, y_0, sigma_x, sigma_y,..)
Optimizer
Data from Experiment
2D Gaussian Profile (x_0, y_0, sigma_x, sigma_y,..)

## Slide 6: Demo of Fit with Experimental Data
Data obtained with free-standing ‘spider-web’ (July 12, 2019, B. Hermann)

## Slide 7: Demo of Fit with Experimental Data
Pro:
Fast
Decent representation of data
Estimation of error
Works as well with less wires
Stable against noise
Con:
Assumption of Gaussian shape
Some details are not reflected

## Slide 8: Alternative Reconstruction: Tomography
Reformulate problem, now: Solve system of linear equations
Applied here: Maximum likelihood – expectation maximization (ML-EM)
Let us look at one iteration of Tomographic Reconstruction…

## Slide 9: Tomographic Reconstruction – One Iteration
Guess of beam profile
Guess of beam profile 𝑋
Apply matrix transform to get projection of current beam profile:
Apply matrix transform to get projection of current beam profile:
𝑌_𝑐𝑢𝑟=𝑀 ∙𝑋
Compute fraction
measured projection / current profile`s projection
Compute fraction
measured projection / current profile`s projection
𝐹= 𝑌/𝑌_𝑐𝑢𝑟
Backprojection step: get correction factor for each pixel
Backprojection step: get correction factor for each pixel
𝐶= 𝑀^𝑇 ∙𝐹
Normalize calculated corrections, multiply to previous guess of profile
Normalize calculated corrections, multiply to previous guess of profile
𝑋=𝑋 ∙𝐶/𝑁
Apply Gaussian kernel to smooth result
Apply Gaussian kernel to smooth result
𝑋=𝐺(𝑋)
With:
beam profile
transform matrix
measured projection
projection of current guess
fraction of measured and current projection
correction factor
Normalization factor
smoothing function

## Slide 10: Tomographic Reconstruction - Applicability
Creation of matrix requires a bit of computation, but: Application of is very fast!
Matrices can be interpolated for measurements with less data points than the matrix supports (This again is comparably fast)
Speeds as high as 600 iterations/s were achieved (on a Laptop from 2012)
Studies of convergence showed that Tomographic reconstruction can lead to better match to the measured data compared to a fit (evaluated using the L1 Norm)

## Slide 11: Tomographic Reconstruction - Demo

## Slide 12: Tomographic Reconstruction – Test for Sub – Micrometer Beams
Beam size here:

## Slide 13: Outlook: Emittance Measurement with Wire Scanner at ACHIP-ATHOS
Measure beam profile at different phase advances
Instead of quad-scan, move hexapod along z (range: +/- 5 cm)
At center: cm
Evolution of around focus:
Phase advance:
Rapid phase advance around small focus
For +/- 5 cm: 157 deg
4D (x, y, x’, y’) Phase space tomography is possible

## Slide 14: Wir schaffen Wissen – heute für morgen
My thanks go to
Dr. Vitaliy Guzenko (LMN)
Benedikt Hermann
Dr. Rasmus Ischebeck
Prof. Dr. Peter Hommelhoff (FAU)
You, my listeners!

## Slide 15: Tomographic Reconstruction – Study of L1 Norm