## Slide 1: Goal: use photon BPM for FOFB i.e. separate e-beam and opt-elems. instabilities
pinkbeam
whitebeam
monochromatic
"standard XBPM"

## Slide 2: Current installations at PXI (pinkbeam) 9/8/2019 first light on SiC XBPM
Pinkbeam
800W (36W)
<1% at 12.4keV
Whitebeams
2kW (5.2mm gap)
80µm C window
Shutter
1th BLADE

## Slide 3: Current installations at PXI (pinkbeam)
2 µm XBPM was installed 1 month ago at PXI pinkbeam (after diamond window).
The measured current is several order of magnitude lower than the expected one.

## Slide 4: Current installations at PXI (pinkbeam) PRELIMINARY RESULTS
FFT of SiC XBPM
FFT of Blades
SiC XBPM
BLADES

## Slide 5: "Long term goal": 1 Development of multifunctional photon XPM
semiconductor based
internal photoemission
array of 4 devices
-- full membrane, -- "high res."
--"small pin-hole": 2.0x1.0mm2
--"blade opening": 3.4x2.2mm2
--"large pin-hole": 6.0x4.0mm2

## Slide 6: "Long term goal": 2 Development of combined position/profile monitor for pinkbeams
pixelated XBM
for beam profile at kHz
2x2 XBM
for beam position @ MHz/nm
copper
GOTTHARD
FEMTO AMP
PINKBEAM

## Slide 7: "Long term goal": 2 Development of combined position/profile monitor for pinkbeams

## Slide 8: Conclusions & outlook
First successful installation of SiC XBPM in pinkbeam location (800W beam power, PXI)
XBPM can be baked, compatible with UHV (1E-10)
Extension towards simulatenous profile&position presented within the AIRES2 call of proposals
Systematic comparison of SiC XBPM with 1th/2th blades. Establishment/test of FOFB based on SiC XBPM