## Slide 1: The magnetic field measurement for the Muon g-2 experiment with precision NMR
drhgfdjhngngfmhgmghmghjmghfmf
Peter Winter
High Energy Physics Division
Argonne National Laboratory

## Slide 2: Overview
Short overview of the E989 Muon g-2 experiment at Fermilab
Measuring in Muon g-2
  NMR technique
  Field mapping with the trolley system
  Field monitoring with the stationary probes
  Absolute field calibration
  Muon convolution
  Systematic, systematics, systematics, ...
Field analysis flow and status for Run-1

## Slide 3
Short overview of The e989 g-2 experiment at fermilab

## Slide 4: Muons in a storage ring (no e field yet)
Cyclotron frequency:
Spin precession frequency:
Larmor + Thomas precession

## Slide 5: Muons in B & E fields with EDM
Assuming b∙B = b∙E = 0:
No E field: E = 0 Weak magnetic focusing
J-PARC E34
Magic momentum (g = 29.3) E field for vertical focusing
CERN-III, BNL E821, Fermilab E989
NO wa oscillation (E ≃ amBcbg2) Only radial E field needed
PSI muonEDM

## Slide 6: Muons in B & E fields with EDM
Assuming b∙B = b∙E = 0, induced electric field :
Fermilab E989
J-PARC E34
PSI muonEDM
and fields
field only
and fields
Measuring the anomalous moment am (neglecting the EDM) requires both a precision measurement of:
  the anomalous spin precession frequency wa
  the magnetic field B
wa = e/m am B

## Slide 7: muon injection & storage: Storage ring magnet
Superconducting coils, C-shaped yoke, 1.45T field strength
Shim toolkit:
  48 top / bottom hats to tune dipole
  800 wedge shims to tune dipole
  edge shims to tune quad and sextupole
  ~9000 iron foils to fine tune field
Power supply feedback to stabilize dipole
~200 tunable coils to shim average higher multipoles
m

## Slide 8: muon injection & storage: Inflector magnet
Inflector magnet cancels main field for muon injection through yoke
Small aperture limits muon flux
Muons injected with 77mm offset from ideal orbit
m
Inflector top view
Inflector cross section

## Slide 9: muon injection & storage: Kicker magnet
3 kicker magnets changes muon angle to bring closer to ideal orbit
Deliver pulse in <149 ns (muon revolution time)
m
Kicker plates

## Slide 10: muon injection & storage: electrostatic quadrupoles
Main B field provides radial focusing
Four electrostatic quadrupoles cover 43% of the storage ring for vertical focusing
Also used to scrape the beam after injection with circular collimators
m
-
-
+
+
-
-
Quadrupole plates

## Slide 11: Measuring wa: calorimeter & Laser calibration
24 calorimeter stations:
  54 PbF2 crystals per station
  SiPM readout for each crystal
  800 MSPS signal digitization
Laser calibration system:
  Each crystal receives laser pulse
  Several monitors to correct for laser fluctuations
  Demonstrated gain corrected to 10-4/h
m

## Slide 12: Precision goals for wa AND wp
ωp goal: Factor of 2.5 Improvement |  | 
Category | E821 (ppb) | E989 Goal (ppb)
Field Calibration | 50 | 35
Trolley Measurements | 50 | 30
Fixed Probe Interpolation | 70 | 30
Muon Convolution | 30 | 10
Time-Dependent Fields | – | 5
Others | 100 | 50
Quadrature Sum | 170 | 70
ωa goal: Factor of 3 Improvement |  | 
Category | E821 (ppb) | E989 Goal (ppb)
Gain Changes | 120 | 20
Lost Muons | 90 | 20
Pileup | 80 | 40
Horizontal CBO | 70 | < 30
E-field/pitch | 110 | 30
Quadrature Sum | 214 | 70
Key upgrades for wa:
  Segmented calorimeters
  New laser calibration system
  Better kicker and quadrupoles
  In-vacuum straw trackers
  New fast digitization & DAQ
  ...
Key upgrades for wp:
  New fixed NMR probes with signal digitization
  Upgraded field mapping trolley with signal digitization
  Improved calibration probe
  Better magnet homogeneity
  ...

## Slide 13
Measuring in muon g-2

## Slide 14: Measuring wp: How the pieces come together
How do we measure the magnetic field?
w

## Slide 15: How do we measure the field: NMR
Nuclear Magnetic Resonance (NMR)
  Extremely precise (~1 ppb)
  Can be very accurate (<35 ppb)
  Measures only the total field B
Use a proton-rich sample...
RF pulse tips proton magnetization by p/2
Precessing protons induce EMF in same coils
...in a magnetic field
H
RF
Voltage (V)
Time (ms)
Muon g-2 NMR probe w/o shield

## Slide 16: Measuring wp: How the pieces come together
How do we measure the magnetic field where the muons are?
w

## Slide 17: The trolley: in-vacuum field mapper
The trolley is equipped with 17 NMR probes with the main goal:
Provides the magnetic field B0 averaged over the muon storage region with a precision of 30 ppb. This is used to calibrate the fixed probe.
Position determination requirement: ±0.5 mm transverse, ±5mm longitudinal
Electronics
NMR probes

## Slide 18: The trolley: in-vacuum field mapper
Coax cable
delivers power,
receives NMR
signals
Two motors /driver pull trolley through muon storage region
17 probes measure at 9000 locations around the ring
This provides a fine field map of the magnetic field B

## Slide 19: New trolley assembly
Trolley electronics centered around low-power SmartFusion chip which has an integrated ARM processor and FPGA
Total power <1 W including new barcode reader

## Slide 20: The trolley: in-vacuum field mapper
Successful and repeatable motion
Azimuthally averaged B(x,y) [ppm]
High-precision
field measurements
Trolley NMR, new motion control and barcode reader all working well
100+ successful trolley field maps
NMR precision is <1 ppb (goal <20 ppb)

## Slide 21: Measuring wp: How the pieces come together
How do we measure the magnetic field while muons are stored?
w
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m

## Slide 22: The fixed probes: Field monitoring at all times
378 NMR probes in fixed locations
Constantly monitor the field with ~1Hz
Each probe readout by ADC (10 MSPS)
Most probes have uncertainty < 30 ppb

## Slide 23: Measuring wp: How the pieces come together
How do we calibrate the magnetic field measurement?
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
w
p

## Slide 24: Water-based NMR calibration probe
Special water probe(s) deliver the absolute calibration in terms of the free proton precession frequency wp
Shift from field felt by free protons compared to protons in water. Goal to have an accuracy of <35ppb
Calibrates the trolley probes with a precision of 30 ppb
Minimal effect from materials and other sources: ds = -5.5 ± 12.9
Very high resolution of 100 ppt / shot
24
1 ppb

## Slide 25: Water-based NMR calibration probe
3D translation stage with non-magnetic materials for in-vacuum operation
The calibration inside the storage ring requires probe position accuracy ≤ 1 mm
25

## Slide 26: Measuring wp: How the pieces come together
How do we fold in the muon distribution?
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
w
p
~

## Slide 27: Averaging over the muon distribution
The field B(r,q,f) measured in the storage region needs to be convoluted with the muon distribution M(r,q,f)
Method 1: Average over f and express B(r,q) and M(r,q) in terms of multipoles and moments:
Method 2: Track the muons M(r,q,f) in the full field map B(r,q,f) with GEANT4 simulation to determine the effective field.

## Slide 28: Measuring wp: How the pieces come together
Systematics, ...
Systematic uncertainties
DB(T)
dB/dx
DBcalib
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
w
p
~

## Slide 29: MAIN Systematics for the Calibration: Field Gradients, DRIFT, and position
gradients
position
Systematics
stability
calib. time
(gross exaggeration)
We want:
But:
g-2 pole
Calibration in MRI magnet and specially shimmed region in g-2
Trolley calibration uncertainty in E821: 90 ppb
Goal for FNAL: 30 ppb

## Slide 30: relative Probe alignment: DB method with linear gradients
Measure with the first probe the bare field Bbare(x0)
Add a linear gradient B0 + Bg*x and measure Bg(x0) = Bbare(x0) + B0 + Bg*x0
The difference DB(x0) = Bg(x0) - Bbare(x0) = B0 + Bg*x0 is unique for each location x0
Repeat steps 1-3 with second probe and reposition until you find the same DB(x0).
x
Probe
Bbare(x0)
Bg(x0)
DB(x0)

## Slide 31: TEST solenoid at ANL for calibration
Installed a former MRI magnet (0-4 Tesla) at ANL
Achieved superb homogeneity and stability:
  1 ppb/mm local gradients
  Drift ~10 ppb / hour
Can impose linear gradients in x, y, z
Magnet used for:
  Systematics for g-2 NMR measurement
  Cross-calibration for g-2
  Hall probe calibration (Mu2e)
  Detector tests
  ...

## Slide 32: Measuring wp: How the pieces come together
Systematics, systematics, ...
Systematic uncertainties
DB(T)
dB/dx
DBcalib
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
w
p
~
Radial field
Shimming
Field
stabilization

## Slide 33: Homogeneity is key to reduce FIELD systematics
Field vs. Azimuth
Azimuthally Averaged
Field vs r,z
Bennett et al. 10.1103/PhysRevD.73.072003
Goal: +/- 25 ppm
Goal: +/- 0.5 ppm

## Slide 34: SHIMMING TOOLS
Multipurpose instrument
  25 NMR Probes for field
  4 capacitive gap sensors
    Measure pole alignment
    70 nm resolution
    Few micron reproducibility
Laser-tracked with mm resolution

## Slide 35: Passive SHIMMING FOR azimuthal homogeneity
Precision alignment to reach shimming goal:
  72 poles
  840 wedge shims
  9000 thin iron foil laminations
10 months of improving the dipole field in 1 minute...
Shimming completed with DB < ±25 ppm ✓
Calibrations Poles Wedges Laminations

## Slide 36: ACTIVE SHIMMING FOR transverse homogeneity and drift stabilization
200 continuous current traces around the ring individuall tunable between +-2A
Used to cancel higher multipoles
Power supply feedback stabilizes main dipole field to ±15 ppb
Azimuthally averaged B(x,y) [ppm]
kHz

## Slide 37: Measuring wp: How the pieces come together
60 Hz
1 kHz
Fast transients
15Hz
130 s
Systematics, systematics, systematics ...
Systematic uncertainties
DB(T)
dB/dx
DBcalib
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
w
p
~
Radial field
Shimming
Field
stabilization

## Slide 38: Measuring transient fields: Fluxgates
Fast detectors for signals up to 10G with bandwidth 1 kHz
Monitors fast field transients not measured by slow NMR
Very helpful in hunting various spikes in the dipole field (malfunctioning strain gauges)

## Slide 39: Measuring transient fields: Vibrating quadrupole plates
Electrostatic quadrupole plates are being pulsed with the muon arrival
Pulsing of plates causes mechanical vibration which generates a magnetic field
Field is seen by the muons and fixed probes but not by the trolley (quad pulsing is turned off)
Dedicated development of new NMR probe that can measure field inside the quads

## Slide 40: Measuring wp: How the pieces come together
Systematics, systematics, systematics, systematics, ...
?
3He
Consistency checks
?
60 Hz
1 kHz
Fast transients
15Hz
130 s
Systematic uncertainties
DB(T)
dB/dx
DBcalib
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
m
w
p
~
Radial field
Shimming
Field
stabilization

## Slide 41: Cross-calibration efforts: 3He NMR and US/japan collaboration
Consistency check of the water-based NMR calibration:
  Use a very homogeneous and stable 1.45T field at Argonne
  Collaborators at University of Michigan have developed a 3He NMR probe with different systematics
  3-years effort to cross-calibrate E989 pulsed-NMR probe with J-PARC Muon g-2/EDM cw-NMR probe (1.45T, 1.7T, 3T)
US/Japan cross-calibration in 2019
3He NMR signal

## Slide 42
FIELD analysis flow and run-1 status

## Slide 43: Magnetic field flow summary
Precisely
measured
Precisely known for probe
inside g-2 ring
inside MRI solenoid
Trolley calibrates fixed probes, measures Bμ.
Fixed probes monitor field drift during
muon storage
Absolute calibration
Trolley relative calibration
Vacuum chamber cross section
Field homogeneity, stability critically affect uncertainty in these processes
Minimized
for probe

## Slide 44
t
0°
360°
180°
t0
B0(t0)
B1n(t0)
B1s(t0)
B2n(t0)
B2s(t0)
B3n(t0)
B3s(t0)
44
dipole: B0
normal quad: B1n
skew quad: B1s
normal sext.: B2n
skew sext.: B2s
normal oct.: B3n
skew oct.: B3s

## Slide 45: Typical Run-1 trolley field map
very uniform
RMS ~20ppm
Trolley maps the field every 2-3 days

## Slide 46
0°
360°
180°
t0
B0(t0)
B1n(t0)
B1s(t0)
B2n(t0)
B2s(t0)
B3n(t0)
B3s(t0)
t1
B0(t1)
B1n(t1)
B1s(t1)
B2n(t1)
B2s(t1)
t3
B0(t3)
B1n(t3)
B1s(t3)
B2n(t3)
B2s(t3)
t
t5
B0(t5)
B1n(t5)
B1s(t5)
B2n(t5)
B2s(t5)
B3n(t5)
B3s(t5)
t4
B0(t4)
B1n(t4)
B1s(t4)
B2n(t4)
B2s(t4)
t2
B0(t2)
B1n(t2)
B1s(t2)
B2n(t2)
B2s(t2)
46

## Slide 47: Field monitoring between trolley maps
Trolley maps the field every 2-3 days
In between trolley field maps, the 72 fixed probe stations track the lower order multipoles (mainly the dipole field). Some of the challenges include:
  Trolley footprint removal to tie fixed probe reading to trolley map
  Limited tracking of higher multipoles by the fixed probes
trolley runs
Fixed probe tracking
Blinded Dipole Moment [ppm]
PRELIMINARY

## Slide 48
0°
360°
180°
t0
t1
t2
t3
t4
t5
B0(t0)
B1n(t0)
B1s(t0)
B2n(t0)
B2s(t0)
B3n(t0)
B3s(t0)
B0(t1)
B1n(t1)
B1s(t1)
B2n(t1)
B2s(t1)
wp
t
B0(t3)
B1n(t3)
B1s(t3)
B2n(t3)
B2s(t3)
B0(t5)
B1n(t5)
B1s(t5)
B2n(t5)
B2s(t5)
B3n(t5)
B3s(t5)
B0(t4)
B1n(t4)
B1s(t4)
B2n(t4)
B2s(t4)
B0(t2)
B1n(t2)
B1s(t2)
B2n(t2)
B2s(t2)
48

## Slide 49: Run-1 absolute calibration
Trolley maps the field every 2-3 days
In between trolley field maps, the 72 fixed probe stations track the lower order multipoles (mainly the dipole field)
A few times, the calibration probe is used to determine the absolute frequency offsets of the trolley probes. Calibration must also account for probe material effects
Trolley Probe

## Slide 50
0°
360°
180°
t0
t1
t2
t3
t4
t5
B0(t0)
B1n(t0)
B1s(t0)
B2n(t0)
B2s(t0)
B3n(t0)
B3s(t0)
B0(t1)
B1n(t1)
B1s(t1)
B2n(t1)
B2s(t1)
wp
t
B0(t3)
B1n(t3)
B1s(t3)
B2n(t3)
B2s(t3)
B0(t5)
B1n(t5)
B1s(t5)
B2n(t5)
B2s(t5)
B3n(t5)
B3s(t5)
B0(t4)
B1n(t4)
B1s(t4)
B2n(t4)
B2s(t4)
B0(t2)
B1n(t2)
B1s(t2)
B2n(t2)
B2s(t2)
50
⊗
wp
~
⊗
wp
~
⊗
wp
~
⊗
wp
~
⊗
wp
~
⊗
wp
~

## Slide 51: Run-1 analysis status: wp
Trolley maps the field every 2-3 days
In between trolley field maps, the 72 fixed probe stations track the lower order multipoles (mainly the dipole field)
A few times, the calibration probe is used to determine the absolute frequency offsets of the trolley probes. Calibration must also account for probe material effects
Multiple analyses ongoing for trolley calibration, fixed probe-trolley interpolation, and systematic uncertainties

## Slide 52: Run-1 analysis status: wp
Trolley maps the field every 2-3 days
In between trolley field maps, the 72 fixed probe stations track the lower order multipoles (mainly the dipole field)
A few times, the calibration probe is used to determine the absolute frequency offsets of the trolley probes. Calibration must also account for probe material effects
Multiple analyses ongoing for trolley calibration, fixed probe-trolley interpolation, and systematic uncertainties
Additional effort to study if we can extract more information from the spatially dense B-field map to deduce the vector components (toroidal harmonics as a solution to Maxwell’s equations for storage ring geometry)
...

## Slide 53: Overall status and outlook
Without data-quality cuts (DQC)
Run-1:
  Analysis ongoing (~1.1 BNL statistics)
  First publication expected in the next months
Run-2:
  Collected ~1.8 BNL statistics (after data quality cuts)
  Analysis efforts starting now in parallel with Run-1 analysis
Summer shutdown 2019:
  Performed several upgrades over the summer (kicker, hall cooling, ...)
Run-3:
  Started in November 2019 to May 2020
  Expected to collect >10 BNL statistics, already >2 BNL on tape
Proposed Run-4:
  Would share beam with mu2e commissioning
Run-3
Run-4
Run-1
& 2
Thank you and stay tuned for the first result...