## Slide 1: Maloja Setup
Photon spectrometer (SLS, T. Schmitt)
Ion Time-of-Flight spectrometer
Beam manipulation and zone plates
Electron analyzer

## Slide 2: Photon Energy Calibration with Electron Spectrometer
Ar(2p-1) Auger electrons
Ar(2p) photo electrons at 540 eV
Energy scan 2 eV increment
Photo electrons

## Slide 3: Single Shot Spectra
Photo electron spectrum Ne(2s)
Photon spectrum

## Slide 4: Single Shot Spectra
Photons
Photo Electrons

## Slide 5: Zone Plate Focus for Electron Spectrometer
XFEL
Zone plate focus in chamber
ca 30um
Electron spectra were greatly improved with focused beam
No multi-photon signal yet
Zone plate for 530 eV
Zone plate for 870 eV
YAG, 10 mm x 10 mm, 20 um thick
Zone plate for 1000 eV
~12 mm
~12 mm
Zone plates: Florian Doering, Christian David

## Slide 6: Harmonic Content!?
Neon photo ion spectrum at 540 eV
Ne+
Ne2+
Ne3+
Only Ne+. expected!
Attenuation with aluminium foil indicates that beam contains significant amount of 3rd harmonic

## Slide 7: Beam Feedback Capabilities
Photon energy absolute via electron spectrometer
Photon spectrum relative (width, shape and shift) over multi-shot average and single shot with photon and electron spectrometer
Pulse energy arriving at endstation and behind sample with all spectrometers
Harmonic content in beam