SwissFEL Porthos, visions for the future
Thomas Schietinger :: Paul Scherrer Institut
Summary of Photon Science Workshop
and Design Implications
Porthos Machine Working Group Meeting, 22 September 2020

---
Photon Science Workshop on Porthos
- 11 September (on Zoom)
- Material on INDICO (https://indico.psi.ch/event/9145)
- Fields covered:
  - Single-shot ultrafast ptychography
  - Ultrafast 3D imaging
  - Time-resolved structural biology
  - Quantum matter
  - Time-resolved chemistry
  - Chemical imaging with incoherently scattered light
  - Stimulated spectroscopy for operando studies
  - Gas-phase scattering of molecular systems
  - From thermal to non-thermal processes
  - Nonlinear and ultra-strong field interaction phenomena
LSF
“cooked &
uncooked”
ideas

---
Photon requirements (Marco's summary)

---
Machine wish list (my summary)
Property	Absolute must	Desirable
Photon energy	up to 20 keV	up to 30–35 keV (not so clear how important the gain is compared to 20 keV)
Pulse length	≤ 5 fs	down to 0.1 fs
Polarization	linear	full polarization control / (only requested by quantum matter)
Repetition rate	100 Hz 12/24 h	100 Hz always
Special features	tunable photon energy / high-power pulses / spectral control (incl. large bandwidth 1%) / self-seeding / two colors

---
Design implications
- Photon energy: depending on the upper limit we agree on, the maximum energy will require SC undulators or may be reached with conventional undulators or with a combination. In any case a linac upgrade will most likely be required to reach the requested photon energy range (details see Sven's slides).
- Intra-undulator chicanes (CHIC design): essential to realize short pulses with high intensity as requested.
- Polarization: linear (combined requirements of high photon energy and polarization control seem exceedingly rare)
- Repetition rate: it may be possible to forego true three-bunch operation by applying “smart scheduling” 100/50/50 Hz or 100/90/10 Hz scenarios with 12 h alternation?
  → Save the cost of RF energy loss and additional gun laser?
- Special features: most (if note all) of them can be covered in all scenarios with the planned hardware.

---
How to proceed? (Proposal to be discussed)
- Objective: deliver to the management a set of options with rough price tags.
- Sketch out (optimize) three options based on different technology and covering different photon energy ranges (considering the combined Aramis-Porthos potential):
  1. All conventional undulators (lowest cost and risk)
  2. All SC undulators for highest energy reach (with fundamental)
  3. Mixed conventional and SC undulators
- Determine the price difference between two-bunch operation and three-bunch operation.
- This will result in a total of six options covering different needs in terms of photon energy and repetition rates.
- Leave it to the management to decide what price we are willing to pay for which features!

---
Acknowledgements
Thank you…